## Slide 1: EE/CprE/SE 491 – Senior Design I and Professionalism
New Simulation Methods to More Effectively Integrate High Levels of Renewable Energy Resources
By: Jared Rickard, Jeremy Nash, Nidhi Rawell, Collins Ntwali
Team Number: 21
Client: MISO
Advisor: Dr. James McCalley
Team Email: sdmay20-21@iastate.edu
Team Website: http://sdmay20-21.sd.ece.iastate.edu/

## Slide 2
Problem Statement
Final Presentation.2
To research and implement various methods to appropriately reduce the fidelity of data profiles while maintaining an adequate amount of key production cost information.
The study must validate the methods’ reliability and quantify the effects the profile approximation has on simulation runtime and results.
It is expected that the properly designed profile reduction method would make the normal 8760 hours production cost simulation more efficient.

## Slide 3
  Conceptual Sketch
Final Presentation.3
Develop
Develop a software tool that computes different metrics of profile data and clusters the data into representative profiles based on those metrics.
Run
Run PCM simulations of the approximated and un-approximated data and compare the results.
Refine
Refine what metrics are used to cluster data and then run new simulations.
Document
Document what was tested to refine these metrics in a report for our client
Package
Finally package all these different options into a UI that our client can use.

## Slide 4: Functional Requirements
Final Presentation.4
Python script to find approximate data sets
  Data subset returned should be quantitatively "close" to original set.
Methods’ reliability
  PCM simulation of this data subset must reliably forecast key PCM information of an un-approximated profile.
Total computation time
  Reduce PCM simulations from ~72 hours to under 24 hours
Easy to use User-Interface
  Tool design should be easy for an untrained user to test and use.

## Slide 5: Non-functional Requirements
Final Presentation.5
Code Convention
  Readability - Clearly commented and labelled for easy modification
  Modifiability – Modularized for easy upgrades and maintenance.
  Simplicity - Efficient; omit unnecessary functions
Tool Usability
  Short process/steps
  Fast runtime
  User manual
Results
  Reproducible testing
  List of best metrics

## Slide 6: Potential Risks & Mitigation
Final Presentation.6
Limited knowledge in coding, data manipulation, and UI design
  Practice and research what works.
Limited knowledge of power grid data attributes and how to characterize the power grid.
  Communicate with the client about what they would like to see
  Research what others in the field might consider important
Obtaining the software necessary
  Stay in constant communication with the production cost modeling software developer

## Slide 7: Resource/Cost Estimate
Final Presentation.7
Resources
  IDEs to write Python
  Production cost modeling simulation software
  Remote virtual machines to run simulation software
Cost
  Python and related IDEs are free
  We're receiving the simulation software for free on a research license
  Virtual machines have been provided by the ETG for free
  Currently zero cost

## Slide 8: Project Milestones
Final Presentation.8
Complete function to subdivide data profiles
  Evaluated by reviewing code and possibly hand computing test samples
Complete function that clusters data
  Evaluated by reviewing code and trying simple, one-dimensional sample clusters
Run multiple PCM simulations with different approximated data sets
  Evaluated by comparing to results of un-approximated data set
Complete UI
  Evaluated by reviewing code and handing it off to MISO engineers to try and figure out.

## Slide 9: Functional Decomposition
Final Presentation.9
Abstract mathematical instruction set to approximate data
  Divide the input into subsets
  Calculate attributes related to each subset
  Find ideal, imaginary attributes, clustered around what was just calculated
  Find the subsets who are closest to the ideal attribute sets. These are now the ideal subsets
Testing the approximated data
  Calculate percent error of different attributes of approximated data in relation to original data.
  Run approximated data through Production Cost Model (PCM) software
  Write up results in report.

## Slide 10: Detailed Design
Final Presentation.10
Input: N x A CSV set of measured generation and load
Divide the input into L x A subsets
From each of these subsets compute M attributes for each column
Organize into a N/L x A*M matrix of data, such that each row represents an LxA subset and each column is an attribute computed for each subset
x1,1​ | x1,2​ | …​ | x1,A​
x2,1​ | x2,2​ | …​ | x2,A​
…​ | …​ | …​ | …​
xN,1​ | xN,2​ | …​ | xN,A​
L x A sized array
x1,1​ | x1,2​ | …​ | x1,A​
x2,1​ | x2,2​ | …​ | x2,A​
…​ | …​ | …​ | …​
xL,1​ | xL,2​ | …​ | xL,A​
…​ | …​ | …​ | …​
xN,1​ | xN,2​ | …​ | xN,A​
c1,1​ | c1,2​ | c1,3​ | …​ | c1,M*A​
c2,1​ | c2,2​ | c2,3​ | …​ | c2,M*A​
…​ | …​ | …​ | …​ | …​
cN/L,1​ | cN/L,2​ | cN/L,3​ | …​ | cN/L,M*A​

## Slide 11: Detailed Design (cont.)
Final Presentation.11
Detailed Design (cont.)
Find K number of ideal, imaginary attributes, clustered around the attributes just computed
Clustering algorithm
c1,1​ | c1,2​ | c1,3​ | c1,4​ | c1,5​ | …​ | c1,M*A​
c2,1​ | c2,2​ | c2,3​ | c2,4​ | c2,5​ | …​ | c2,M*A​
…​ | …​ | …​ | …​ | …​ | …​ | …​
cN/L,1​ | cN/L,2​ | cN/L,3​ | cN/L,4​ | cN/L,5​ | …​ | cN/L,M*A​
d1,1​ | d1,2​ | d1,3​ | d1,4​ | d1,5​ | …​ | d1,M*A​
…​ | …​ | …​ | …​ | …​ | …​ | …​
dK,1​ | dK,2​ | dK,3​ | dK,4​ | dK,5​ | …​ | dK,M*A​
The clustering algorithm (currently K-Means) interprets each row as a point in M*A-dimensional space and finds K ideal points, returning these points as rows in a K x M*A matrix.
Each row of the original N/L x M*A matrix has a distance to each row of the ideal matrix and each row of the original matrix is “represented” by the closest row of the ideal matrix

## Slide 12: Detailed Design (cont.)
Final Presentation.12
Find the subsets whose attributes are closest to these ideal attribute sets
  We're unable to rebuild a full L x A array from these ideal attributes
Finally we return these ideal L x A subsets and which subsets they represent
  Each L x A array is saved as a new CSV
  A final CSV containing the index of every L x A subset and the index of its best representation is also saved
…
y1,1,1​ | y1,2,1​ | …​ | y1,A,1​
y2,1,1​ | y2,2,1​ | …​ | y2,A,1​
…​ | …​ | …​ | …​
yN,1,1​ | yN,2,1​ | …​ | yN,A,1​
y1,1,k​ | y1,2,k​ | …​ | y1,A,k​
y2,1,k​ | y2,2,k​ | …​ | y2,A,k​
…​ | …​ | …​ | …​
yN,1,k​ | yN,2,k​ | …​ | yN,A,k​

## Slide 13: Detailed Design (cont.)
Final Presentation.13
Example input settings
Example output

## Slide 14: HW/SW/Technology Platform(s) used
Final Presentation.14
Software
  Python for code
  Plexos for production cost modeling (PCM)
  Python integrated development environment (IDE)
Hardware
  Virtual machines provided by the ETG to run simulations remotely

## Slide 15: Test Plan
Final Presentation.15
Prior to Plexos Trials:
Runtime Tests
  Variables are cluster number, attribute number, and subset size
  Keep two constant, test the third
Accuracy Tests
  Total energy and Cap factor
Attribute Tests
  We have six attributes currently, run tests for every combination of the six
  Make sure one attribute doesn't overpower other attributes
During Plexos Trials:
Runtime Tests
  Make sure that simulation runtimes have been dramatically reduced
Accuracy Tests
  Determine how close the results of these shortened runs compare to the original runs
Attribute Tests
  Refine the attribute list based on which runs had the best accuracy from the previous test.

## Slide 16: Prototype Implementations & Test Results
Final Presentation.16
Prototype
  Currently have a Python script that follows the basic instruction set
  Limited options: small choice of attributes, only one clustering algorithm
Test Results
  Examples of testing the Python code's runtime and attributes

## Slide 17: Contributions
Final Presentation.17
Jared Rickard
  Designed instruction set, wrote Python code around steps
Jeremy Nash
  Organized client meetings and meeting notes.
  Tested python code for run-time and accuracy.
Nidhi Rawell
  Researched different clustering methods and various studies related to the project
  Compared the pros and cons of different clustering methods
Collins Ntwali
  Documented findings and progress.
  Contributed to list of attributes/equations.

## Slide 18: Current Project Status
Final Presentation.18
As of Monday, December 9 2019:
  Initial coding is finished
  Recently obtained simulation software
  Some functional testing complete
  Some nonfunctional testing complete

## Slide 19: Plan for next semester
Final Presentation.19
Next step:
  Quantify/Weight attributes of the data
  Simulate the original data profile and as many approximated profiles we can generate using PLEXOS
  Add more attributes and clustering algorithm options
  Develop relationships between input choices and differences in results
  Develop UI

## Slide 20: Thank You!
Team: Jeremy N, Collins N, Nidhi R, Jared R.
Advisor: Dr. James McCalley
Client: Midcontinent Independent System Operator (MISO)
Email: sdmay20-21@iastate.edu
Website: sdmay20-21.sd.ece.iastate.edu
Do you have any questions?